## Slide 1: Benchmarking Quantum Computer
Prabhas Chongstitvatana
Faculty of Engineering
Chulalongkorn University

## Slide 2: Hello World Program
quantum random circuit sampling (RCS) , that is, to approximately sample bitstrings from the output distribution generated by a random quantum circuit.

## Slide 3: Simulation of Quantum Computation
a simulation of the quantum computation, and the computational cost increases exponentially in the number of qubits for quantum circuits of sufficient depth.
Storing the wave function from the output of a random quantum circuit with 40 qubits requires 8.8 TB at single precision (240 × 8 bytes), and 50qubits require 9 PB.

## Slide 4: RCS benchmark
1) Generate random circuits fitted to a given NISQ architecture,
2) Execute random circuits, collecting bitstrings, time to solution, and energy consumption of the quantum computer,
3) Calculate probabilities of collected bitstrings using a classical simulation (qFlex) to measure the NISQ performance or fidelity,
4) Perform a classical noisy simulation (qFlex) based on calculated fidelity to collect equivalent classical computational metrics of relevance – total floating point operations/time-to-solution/power consumption.

## Slide 5: Examples of Quantum Computer
Examples of NISQ devices are
the 50-qubit IBM QPU [32],
the 72-qubit Google Bristlecone QPU

## Slide 6: Quantum Computer Energy Requirement
the main sources of energy consumption are:
- Dilution Refrigerator - because quantum computers operate at around the 15 mK range, a large dilution refrigerator that typically consumes ∼10 kW is necessary.
- Electronic racks - these typically consume around 5 kW of power. They consist of oscilloscopes, microwave electronics, Analog-Digital converters, and clocks.
Therefore a typical quantum computer will consume approximately ∼15 kW of energy for a single QPU of 72 qubits

## Slide 7: Speed of Quantum Computer
the rate at which quantum computers can execute a circuit. In the case of superconducting qubits, the circuit execution rate is approximately 10 kHz to 100 kHz.

## Slide 8: The Big Iron

## Slide 9: Summit
Each node consumes around 2.4 kW of energy
and consists of 2 IBM Power9 CPUs and 6 NVIDIA V100 GPUs,
with a total of 4608 nodes
(1.8 kW per node is consumed by 6 NVIDIA Volta GPUs)

## Slide 10: Performance
qFlex makes use of efficient single-precision matrix-matrix multiplications and an optimized tensor transpose kernel on NVIDIA GPUs
GPU implementation of qFlex reaches a peak performance of 92% and delivers a sustained absolute performance of 68% in simulations spanning the entire Summit supercomputer (281 Pflop/s single precision without mixed-precision acceleration).

## Slide 11: Benchmark

## Slide 12: Result

## Slide 13: Energy

## Slide 14: Bhumipol Dam
ชื่อทางการ เขื่อนภูมิพล
ที่ตั้ง เขาแก้ว อำเภอสามเงา จังหวัดตาก
พิกัดภูมิศาสตร์ 17.265°N 98.9°E
เริ่มต้นการก่อสร้าง พ.ศ. 2500
วันที่เปิด 17 พฤษภาคม พ.ศ. 2507
Dam and spillways
ความสูง 154 เมตร
ความยาว 486 เมตร
ความกว้าง (ที่ฐาน) 56 เมตร
กั้น แม่น้ำปิง
เขื่อนภูมิพลมีกำลังการผลิตติดตั้งทั้งสิ้น ๗๗๙.๒ เมกกะวัตต์ เมื่อวันที่ ๑๗ พฤษภาคม ๒๕๔๕

## Slide 15: More Information
Search “Prabhas Chongstitvatana”
Go to me homepage