## Slide 1
Chapter 1 Computer Networks and the Internet
Computer Networking: A Top Down Approach Featuring the Internet, 2nd edition. Jim Kurose, Keith Ross Addison-Wesley, July 2002.
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in powerpoint form so you can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) in substantially unaltered form, that you mention their source (after all, we’d like people to use our book!)
If you post any slides in substantially unaltered form on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2002
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Chapter 1: Introduction
Our goal:
get context, overview, “feel” of networking
more depth, detail later in course
approach:
  descriptive
  use Internet as example
Overview:
what’s the Internet
what’s a protocol?
network edge
network core
access net, physical media
Internet/ISP structure
performance: loss, delay
protocol layers, service models
history

## Slide 3: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 4: What’s the Internet: “nuts and bolts” view
millions of connected computing devices: hosts, end-systems
  PCs workstations, servers
  PDAs phones, toasters
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate = bandwidth
routers: forward packets (chunks of data)
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 5: “Cool” internet appliances
World’s smallest web server
http://www-ccs.cs.umass.edu/~shri/iPic.html
IP picture frame
http://www.ceiva.com/
Web-enabled toaster+weather forecaster

## Slide 6: What’s the Internet: “nuts and bolts” view
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, FTP, PPP
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 7: What’s the Internet: a service view
communication infrastructure enables distributed applications:
  Web, email, games, e-commerce, database., voting, file (MP3) sharing
communication services provided to apps:
  connectionless
  connection-oriented
cyberspace [Gibson]:
  “a consensual hallucination experienced daily by billions of operators, in every nation, ...."

## Slide 8: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 9: What’s a protocol?
a human protocol and a computer network protocol:
Q: Other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
req
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time

## Slide 10: A closer look at network structure:
network edge: applications and hosts
network core:
  routers
  network of networks
access networks, physical media: communication links

## Slide 11: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 12: The network edge:
end systems (hosts):
  run application programs
  e.g. Web, email
  at “edge of network”
client/server model
  client host requests, receives service from always-on server
  e.g. Web browser/server; email client/server
peer-peer model:
  minimal (or no) use of dedicated servers
  e.g. Gnutella, KaZaA

## Slide 13: Network edge: connection-oriented service
Goal: data transfer between end systems
handshaking: setup (prepare for) data transfer ahead of time
  Hello, hello back human protocol
  set up “state” in two communicating hosts
TCP - Transmission Control Protocol
  Internet’s connection-oriented service
TCP service [RFC 793]
reliable, in-order byte-stream data transfer
  loss: acknowledgements and retransmissions
flow control:
  sender won’t overwhelm receiver
congestion control:
  senders “slow down sending rate” when network congested

## Slide 14: Network edge: connectionless service
Goal: data transfer between end systems
  same as before!
UDP - User Datagram Protocol [RFC 768]: Internet’s connectionless service
  unreliable data transfer
  no flow control
  no congestion control
App’s using TCP:
HTTP (Web), FTP (file transfer), Telnet (remote login), SMTP (email)
App’s using UDP:
streaming media, teleconferencing, DNS, Internet telephony

## Slide 15: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 16: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 17: Network Core: Circuit Switching
End-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required

## Slide 18: Network Core: Circuit Switching
network resources (e.g., bandwidth) divided into “pieces”
pieces allocated to calls
resource piece idle if not used by owning call (no sharing)
dividing link bandwidth into “pieces”
  frequency division
  time division

## Slide 19: Circuit Switching: TDMA and TDMA
FDMA
frequency
time
TDMA
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 20: Network Core: Packet Switching
each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed
resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  transmit over link
  wait turn at next link
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 21: Packet Switching: Statistical Multiplexing
Sequence of A & B packets does not have fixed pattern  statistical multiplexing.
In TDM each host gets same slot in revolving TDM frame.
A
B
C
10 Mbs
Ethernet
1.5 Mbs
D
E
statistical multiplexing
queue of packets
waiting for output
link

## Slide 22: Packet switching versus circuit switching
1 Mbit link
each user:
  100 kbps when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active less than .0004
Packet switching allows more users to use network!
N users
1 Mbps link

## Slide 23: Packet switching versus circuit switching
Great for bursty data
  resource sharing
  simpler, no call setup
Excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 6)
Is packet switching a “slam dunk winner?”

## Slide 24: Packet-switching: store-and-forward
Takes L/R seconds to transmit (push out) packet of L bits on to link or R bps
Entire packet must arrive at router before it can be transmitted on next link: store and forward
delay = 3L/R
Example:
L = 7.5 Mbits
R = 1.5 Mbps
delay = 15 sec
R
R
R
L

## Slide 25: Packet Switching: Message Segmenting
Now break up the message into 5000 packets
Each packet 1,500 bits
1 msec to transmit packet on one link
pipelining: each link works in parallel
Delay reduced from 15 sec to 5.002 sec

## Slide 26: Packet-switched networks: forwarding
Goal: move packets through routers from source to destination
  we’ll study several path selection (i.e. routing)algorithms (chapter 4)
datagram network:
  destination address in packet determines next hop
  routes may change during session
  analogy: driving, asking directions
virtual circuit network:
  each packet carries tag (virtual circuit ID), tag determines next hop
  fixed path determined at call setup time, remains fixed thru call
  routers maintain per-call state

## Slide 27: Network Taxonomy
Telecommunication
networks
Circuit-switched
networks
FDM
TDM
Packet-switched
networks
Networks
with VCs
Datagram
Networks
Datagram network is not either connection-oriented
or connectionless.
Internet provides both connection-oriented (TCP) and
connectionless services (UDP) to apps.

## Slide 28: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 29: Access networks and physical media
Q: How to connection end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 30: Residential access: point to point access
Dialup via modem
  up to 56Kbps direct access to router (often less)
  Can’t surf and phone at same time: can’t be “always on”
ADSL: asymmetric digital subscriber line
  up to 1 Mbps upstream (today typically < 256 kbps)
  up to 8 Mbps downstream (today typically < 1 Mbps)
  FDM: 50 kHz - 1 MHz for downstream
  4 kHz - 50 kHz for upstream
  0 kHz - 4 kHz for ordinary telephone

## Slide 31: Residential access: cable modems
HFC: hybrid fiber coax
  asymmetric: up to 10Mbps upstream, 1 Mbps downstream
network of cable and fiber attaches homes to ISP router
  shared access to router among home
  issues: congestion, dimensioning
deployment: available via cable companies, e.g., MediaOne

## Slide 32: Residential access: cable modems
Diagram: http://www.cabledatacomnews.com/cmic/diagram.html

## Slide 33: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)
Typically 500 to 5,000 homes

## Slide 34: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)

## Slide 35: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
server(s)

## Slide 36: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
FDM:

## Slide 37: Company access: local area networks
company/univ local area network (LAN) connects end system to edge router
Ethernet:
  shared or dedicated link connects end system and router
  10 Mbs, 100Mbps, Gigabit Ethernet
deployment: institutions, home LANs happening now
LANs: chapter 5

## Slide 38: Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  802.11b (WiFi): 11 Mbps
wider-area wireless access
  provided by telco operator
  3G ~ 384 kbps
    Will it happen??
  WAP/GPRS in Europe
base
station
mobile
hosts
router

## Slide 39: Home networks
Typical home network components:
ADSL or cable modem
router/firewall/NAT
Ethernet
wireless access
point
wireless
access
point
wireless
laptops
router/
firewall
cable
modem
to/from
cable
headend
Ethernet
(switched)

## Slide 40: Physical Media
Bit: propagates between transmitter/rcvr pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
Twisted Pair (TP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps Ethernet
  Category 5 TP: 100Mbps Ethernet

## Slide 41: Physical Media: coax, fiber
Coaxial cable:
two concentric copper conductors
bidirectional
baseband:
  single channel on cable
  legacy Ethernet
broadband:
  multiple channel on cable
  HFC
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 5 Gps)
low error rate: repeaters spaced far apart ; immune to electromagnetic noise

## Slide 42: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
Radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., WaveLAN)
  2Mbps, 11Mbps
wide-area (e.g., cellular)
  e.g. 3G: hundreds of kbps
satellite
  up to 50Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus LEOS

## Slide 43: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 44: Internet structure: network of networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., UUNet, BBN/Genuity, Sprint, AT&T), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately
NAP
Tier-1 providers also interconnect at public network access points (NAPs)

## Slide 45: Tier-1 ISP: e.g., Sprint
Sprint US backbone network

## Slide 46: Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other, interconnect at NAP

## Slide 47: Internet structure: network of networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 48: Internet structure: network of networks
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 49: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 50: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 51: Four sources of packet delay
1. nodal processing:
  check bit errors
  determine output link
A
B
propagation
transmission
nodal
processing
queueing
2. queueing
  time waiting at output link for transmission
  depends on congestion level of router

## Slide 52: Delay in packet-switched networks
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantities!

## Slide 53: Caravan analogy
Cars “propagate” at 100 km/hr
Toll booth takes 12 sec to service a car (transmission time)
car~bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
Time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
Time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 54: Caravan analogy (more)
Cars now “propagate” at 1000 km/hr
Toll booth now takes 1 min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at 1st booth?
Yes! After 7 min, 1st car at 2nd booth and 3 cars still at 1st booth.
1st bit of packet can arrive at 2nd router before packet is fully transmitted at 1st router!
  See Ethernet applet at AWL Web site
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 55: Nodal delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs

## Slide 56: Queueing delay (revisited)
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 57: “Real” Internet delays and routes
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 58: “Real” Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
Three delay measements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no reponse (probe lost, router not replying)
trans-oceanic
link

## Slide 59: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
when packet arrives to full queue, packet is dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not retransmitted at all

## Slide 60: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 61: Protocol “Layers”
Networks are complex!
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of organizing structure of network?
Or at least our discussion of networks?

## Slide 62: Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 63: Organization of air travel: a different view
Layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 64: Layered air travel: services
Counter-to-counter delivery of person+bags
baggage-claim-to-baggage-claim delivery
people transfer: loading gate to arrival gate
runway-to-runway delivery of plane
airplane routing from source to destination

## Slide 65: Distributed implementation of layer functionality
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
Departing airport
arriving airport
intermediate air traffic sites
airplane routing
airplane routing

## Slide 66: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 67: Internet protocol stack
application: supporting network applications
  FTP, SMTP, STTP
transport: host-host data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  PPP, Ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 68: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
Each layer:
distributed
“entities” implement layer functions at each node
entities perform actions, exchange messages with peers

## Slide 69: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data
E.g.: transport
take data from app
add addressing, reliability check info to form “datagram”
send datagram to peer
wait for peer to ack receipt
analogy: post office
data
transport
transport
ack

## Slide 70: Layering: physical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data

## Slide 71: Protocol layering and data
Each layer takes data from above
adds header information to create new data unit
passes new data unit to layer below
application
transport
network
link
physical
application
transport
network
link
physical
source
destination
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
message
segment
datagram
frame

## Slide 72: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 ISPs and Internet backbones
  1.6 Delay & loss in packet-switched networks
  1.7 Internet structure and ISPs
  1.8 History

## Slide 73: Internet History
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet demonstrated publicly
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 74: Internet History
1970: ALOHAnet satellite network in Hawaii
1973: Metcalfe’s PhD thesis proposes Ethernet
1974: Cerf and Kahn - architecture for interconnecting networks
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets

## Slide 75: Internet History
1983: deployment of TCP/IP
1982: SMTP e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: FTP protocol defined
1988: TCP congestion control
new national networks: Csnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks

## Slide 76: Internet History
Early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
Late 1990’s – 2000’s:
more killer apps: instant messaging, peer2peer file sharing (e.g., Naptser)
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000’s: commercialization, the Web, new apps

## Slide 77: Introduction: Summary
Covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
Internet/ISP structure
performance: loss, delay
layering and service models
history
You now have:
context, overview, “feel” of networking
more depth, detail to follow!