## Slide 1: Flynn’s Taxonomy 2110732 Parallel Computing
Veera Muangsin, Ph.D.
Natawut Nupairoj, Ph.D.
ISEL Laboratory

## Slide 2: Architecture & Components
Processor
Memory
Cache
Disk
P
Network Interface Circuitry
Processor + Cache
Directory
M
C
D
NIC
P/C
DIR

## Slide 3: PC Architecture
P/C
M
D
NIC

## Slide 4: Flynn’s Taxonomy
Very influential paper in 1966.
Two most important characteristics
  Number of instruction streams.
  Number of data elements.
  SISD (Single Instruction, Single Data).
  SIMD (Single Instruction, Multiple Data).
  MISD (Single Instruction, Single Data).
  MIMD (Multiple Instruction, Multiple Data).

## Slide 5: SISD
One instruction stream and one data stream - from memory to processor.
von Neumann’s architecture.
Example
  PC.
P
M
I, D

## Slide 6: Von Neumann Architecture
Invented by John von Neumann (Hungarian) 40 years ago.
Stored-program concept
  CPU executes a stored program that specifies a sequence of read and write operations on the memory.
A lot of traffic between CPU and memory
  Flynn Bottleneck.

## Slide 7: Basic Von Neumann Design
  Memory is used to store both program and data instructions
  Program instructions are coded data which tell the computer to do something
  Data is simply information to be used by the program
  A central processing unit (CPU) gets instructions and/or data from memory, decodes the instructions and then sequentially performs them.

## Slide 8: SISD Characteristics
A serial (non-parallel) computer
Single instruction: only one instruction stream acted on by the CPU during any one clock cycle
Single data: only one data stream as input during any one clock cycle.

## Slide 9: SIMD
One control unit tells processing elements to compute (at the same time).
Examples
  TMC/CM-1, Maspar MP-1.
P
M
D
P
M
D
P
M
D
P
M
D
Ctrl
I

## Slide 10: SIMD Characteristics
Single instruction: All nodes execute the same instruction at any given clock cycle.
Multiple data: Each node can operate on a different data element.
Need instruction dispatcher.
For problems with a high degree of regularity, such as image processing.
Synchronous (lockstep) – ILP/Fine-grain.
Two varieties: Processor Arrays and Vector Pipelines.

## Slide 11: MISD
No one agrees if there is such a MISD.
Some say systolic array and pipeline processor are.
P
D
P
D
P
D
D
I
I
I

## Slide 12: MIMD
Multiprocessor, each executes its own instruction/data stream.
May communicate with one another once in a while.
Examples
  IBM SP, SGI Origin, HP Convex, Cray ...
P
M
I, D
P
M
I, D
P
M
I, D
P
M
I, D
N
E
T
W
O
R
K

## Slide 13: MIMD Characteristics
Multiple Instruction: every processor may be executing a different instruction stream.
Multiple Data: every processor may be working with a different data stream.
Execution can be synchronous or asynchronous.

## Slide 14: SPMD
MIMD is good, but too complicated.
Single Program Multiple Data
  Combination of MIMD and SIMD.
  All nodes run the same program (SIMD)
    Simpler to write and understand.
  All nodes runs at its own pace (MIMD).
    Process-level parallelism, medium/coarse grain
    No dispatcher.
    Use synchronization
    Communication become very important.