## Slide 1: Parallel Architecture 2110732 Parallel Computing
Veera Muangsin, Ph.D.
Natawut Nupairoj, Ph.D.
ISEL Laboratory

## Slide 2: Parallel Architecture
SMP-Symmetric Multiprocessor.
PVP-Parallel Vector Processor.
MPP-Massively Parallel Processor.
DSM-Distributed Shared Memory.
NOWs/COWs
  Network of Workstations.
  Cluster of Workstations.

## Slide 3: Symmetric Multi-Processor
Bus or Crossbar
P/C
P/C
P/C
P/C
M
M
M
M

## Slide 4: SMP
Strengths
  Simple and low cost.
  Low synchronization overhead.
Weaknesses
  Do not scale. Usually from 2 (2-way) to 64 processors (64-way).
Examples
  PCs, IBM R50, SGI Power Challenge, Alpha Server.

## Slide 5: Dell’s Intel Xeon SMP

## Slide 6: Sun Fire E25K

## Slide 7: Sun Fire E25K

## Slide 8: Parallel Vector Processor
Similar to SMP but with vector CPUs.
Strengths
  High performance, suitable for scientific computation.
Weakness
  Expensive, proprietary.
Examples
  Cray C-90, T-90, NEC SX-4.
  Earth Simulator (Vector in MPP).

## Slide 9: Distributed Shared Memory
P/C
M
NIC
P/C
M
NIC
P/C
M
NIC
Interconnection Network
DIR
DIR
DIR

## Slide 10: DSM
Opposite of SMP.
Memory
  Physically distributed.
  Logically shared.
    Special hardware or software (DIR).
Strengths
  Fairly scalable.
  Simple to program.

## Slide 11: DSM
Weaknesses
  Bottleneck.
Examples
  DASH, Cray T3D, Cray T3E.
  Cray X1 (Vector in MPP).

## Slide 12: Cray X1 (up to 4,096 CPUs)

## Slide 13: Massively Parallel Processor
P/C
M
NIC
P/C
M
NIC
P/C
M
NIC
Interconnection Network
Node

## Slide 14: MPP
Hundreds/thousands of nodes.
Custom-designed network
  Tightly coupled.
Strengths
  The most powerful, very high-performance.
  Extremely scalable.

## Slide 15: MPP
Weaknesses
  Very expensive.
  Require lots of care.
Examples
  ASCI.
  Blue Gene.

## Slide 16: Sandia’s ASCI TFLOPS

## Slide 17: NOWs / COWs / Cluster
COTS – Commercial Off-The-Shelf tech.
PCs connecting through high-speed network.
  Node = Processor + Memory + Disk.
  Linux + Fast Ethernet switches.
  Loosely coupled.

## Slide 18: NOWs
Strengths
  Cheap, cheap, cheap.
  Scalable, upgradable.
Weaknesses
  Not powerful.
  Slightly difficult to manage.
  High synchronization overhead.

## Slide 19: NOWs
Examples
  IBM/SP, Beowulf, Berkeley NOW, Digital TruCluster.
  Terascale Cluster (1,100 Mac G5).
  Tungsten (1,250 Dell PowerEdge 1750 and Myrinet-2000).