## Slide 1: Parallelism in CPU 2110732 Parallel Computing
Veera Muangsin, Ph.D.
Natawut Nupairoj, Ph.D.
ISEL Laboratory

## Slide 2: Terminologies
Hazards
  Prevent the next instruction from execution during its designated clock cycle.
  Structural hazards.
  Data hazards: RAW, WAW, WAR.
  Control hazards.
Out-of-order completion.

## Slide 3: Terminologies
Instruction issuing (or scheduling)
  Static scheduling.
  Dynamic scheduling
    Avoid stalling by start executing the next instruction before the current one.
    Out-of-order execution.
    Scoreboard & Tomasulo approach.
Speculative execution
  Execute an instruction before CPU knows that the instruction should execute.
  Branch prediction.

## Slide 5: Branch Prediction
Eliminates many control hazards
  provides "uninterrupted" instruction stream
Example
Static Program:
loop: r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
Dynamic Stream
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0

## Slide 6: Terminologies
Register renaming
  More physical registers than logical registers.
  Turns instruction stream into "single assignment" form
    avoids WAW and WAR hazards.
  For each instruction
    Read source register mappings from table.
    Acquire new result physical register from free pool.
    Modify map table for new result register mapping.
  Example
    Assume 8 logical, 24 physical registers.
    From “Advanced Computer Architecture I” slides by J. E. Smith.

## Slide 7
Fetched Stream
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
Register
MAP
r1 p3
r2 p4
r3 p6
r4 p1
r5 p2
r6 p7
r7 p5
Renamed Stream
Free Pool
p8,p9,p10,p11,p12,p13,
p14,p15,p16,p17,p18,
P19,p20,p21,p22,p23,p24

## Slide 8
Fetched Stream
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
Register
MAP
r1 p3
r2 p4
r3 p6
r4 p1
r5 p2
r6 p7
r7 p5
Renamed Stream
r3 <- mem(p1+p4)
Free Pool
p8,p9,p10,p11,p12,p13,
p14,p15,p16,p17,p18,
P19,p20,p21,p22,p23,p24
1
1

## Slide 9
Fetched Stream
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
Register
MAP
r1 p3
r2 p4
r3 p6
r4 p1
r5 p2
r6 p7
r7 p5
Renamed Stream
p8 <- mem(p1+p4)
Free Pool
p8,p9,p10,p11,p12,p13,
p14,p15,p16,p17,p18,
P19,p20,p21,p22,p23,p24
2

## Slide 10
Fetched Stream
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
Register
MAP
r1 p3
r2 p4
r3 p8
r4 p1
r5 p2
r6 p7
r7 p5
Renamed Stream
p8 <- mem(p1+p4)
Free Pool
p9,p10,p11,p12,p13,
p14,p15,p16,p17,p18,
P19,p20,p21,p22,p23,p24
3

## Slide 11
Fetched Stream
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
Register
MAP
r1 p3
r2 p4
r3 p8
r4 p1
r5 p2
r6 p7
r7 p9
Renamed Stream
p8 <- mem(p1+p4)
p9 <- mem(p2+p4)
Free Pool
p10,p11,p12,p13, p14,p15,
p16,p17,p18,P19,p20,p21,p22,p23,p24

## Slide 12
Fetched Stream
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
Register
MAP
r1 p3
r2 p4
r3 p8
r4 p1
r5 p2
r6 p7
r7 p10
Renamed Stream
p8 <- mem(p1+p4)
p9 <- mem(p2+p4)
r10 <- p9 * p8
Free Pool
p11,p12,p13, p14,p15,
p16,p17,p18,P19,p20,p21,
p22, p23,p24

## Slide 13
Fetched Stream
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
P <- loop; r1!=0
r3 <- mem(r4+r2)
r7 <- mem(r5+r2)
r7 <- r7 * r3
r1 <- r1 - 1
mem(r6+r2)<- r7
r2 <- r2 + 8
Register
MAP
r1 p21
r2 p22
r3 p18
r4 p1
r5 p2
r6 p7
r7 p20
Renamed Stream
p8 <- mem(p1+p4)
p9 <- mem(p2+p4)
r10 <- p9 * p8
p11 <- p3 - 1
mem(p7+p4)<- p10
p12 <- p4 + 8
P <- loop; p11!=0
p13 <- mem(p1+p12)
p14 <- mem(p2+p12)
p15 <- p14 * p13
p16 <- p11 - 1
mem(p7+p12)<- p15
p17 <- p12 + 8
P <- loop; p16!=0
p18 <- mem(p1+p17)
p19 <- mem(p2+p17)
p20 <- p19 * p18
p21 <- p16 - 1
mem(p7+p17)<- p20
p22 <- p17 + 8
Free Pool
p23,p24

## Slide 14: Trends in ILP - Motivation
Improvement in chip manufacturing
  Smaller transistors = more density.
  More logics can be added.
New software availability
  Better compilers – can assist hardware
    Loop unrolling.
    Software pipelining.
    Trace scheduling.
  More sophisticated OS – thread supported.
  Advanced development and testing tools.
Focus on specialized problems
  Multimedia, server, etc.

## Slide 15: Trends in ILP
Superscalar
  Very old, but basic for all trends.
Multimedia extension instruction set
  Also very old.
Very Large Instruction Word
  Old ideas, to-be-implemented as EPIC in Intel Itanium.

## Slide 16: Trends in ILP
Simultaneous Multithreading (SMT)
  New ideas, just implemented in
    Intel Pentium Xeon.
    Intel Pentium-4.
    Compaq EV8 (Alpha 21464).
Chip Multiprocessor (CMP)
  New ideas, just implemented in:
    IBM Power4.
    Sun UltraSparc.

## Slide 17: Superscalar Processors
 Achieve more performance via increased bandwidth
    Instruction Level Parallelism (ILP)
    1 2 3 4 5 6 7 8 9
    i IF ID EX MEM WB
    i+1 IF ID EX MEM WB
    i+2 IF ID EX MEM WB
    i+3 IF ID EX MEM WB
    i+4 IF ID EX MEM WB
    i+5 IF ID EX MEM WB
    i+6 IF ID EX MEM WB
    i+7 IF ID EX MEM WB

## Slide 18: Superscalar Processors
Multiple instruction issues per clock
   superscalar
Often combined with dynamic issue
  although static issue has been done (Alpha 21064)

## Slide 19: The Big Picture

## Slide 20: Elements of Superscalar Processors
High performance instruction fetching
  Multiple instructions per cycle
  Branch and Jump prediction
Dispatch and dependence resolution
  Eliminate "false" dependences (WAR, WAW)
  Set up linkages for true dependences
  e.g. register renaming
Parallel o-o-o instruction issue
Speculative execution

## Slide 21: Elements of Superscalar Processors
Parallel resources:
  functional units, paths, register ports
High performance memory systems
Methods for precise traps

## Slide 22: Superscalar CPUs

## Slide 23: Multimedia Extension
Multimedia applications have common characteristics in basic routines
  Small native data types (8-bit pixels or 16-bit audio samples).
  Localized recurring operations.
  Parallelism.
Implement extended instruction sets on the existing CPUs
  MMX – Pentium.
  SSE – Pentium III.
  3D-Now – AMD.

## Slide 24: MMX Instruction Set
Perform SIMD-like operation
  Single computation on group of data
  Packed data types: 8 bytes, 4 words, 2 double-word, or 1 quad-word.
  Add, sub, compare, multiply, and, or, and-not, xor, move, shift, …
Operate on existing 64-bit floating-point registers
  Ensure backward compatibility.

## Slide 27: Superscalar

## Slide 28: VLIW

## Slide 29: SMT

## Slide 30: CMP