## Slide 1: Programming Graphics Processing Unit
Prabhas Chongstitvatana
Chulalongkorn University

## Slide 2: NPU
a simple GPU with four 32-bit cores
4 Processing Elements (PE or core)
Each PE has 32 registers, one ALU and Local data store (LS)
16Kx32 bits of memory (14-bit address)
Memory Interface (MI) connected to Local Store (LS)
LS communicates to all PEs in parallel
instruction has fixed size of 32 bits

## Slide 3: NPU

## Slide 4: Processing Elements
PEs are similar to general cores
They share the same Program memory (stored program), Program counter and Instruction Register
All PEs run the same instruction

## Slide 5: Processing Elements
Each PE has three distinct units: Register, ALU and Address Unit (AU).
Registers of each PE connects to its Local Store (LS)
AU outputs effective address (for index addressing)

## Slide 6: Memory and Local Store
Memory Interface is a big highway to connect Main Memory to Local Store
moving data Main to LS is a serial operation
moving LS to R is simultaneous for all PEs

## Slide 7: Exchange data between PEs
Two unique instructions for NPU (with respect to CPU)
Load wide (ldw) sends M to all LS at once.
Broadcast (bc) instruction sends an LS to R of all PEs.
This allows PEs to exchange data without going through main memory.

## Slide 8: Instruction set
Instruction format
op:8 a1:14 a2:5 a3:5
Data
ld ls @ads LS[ls] = M[ads] ls = 0,1,2,3
st ls @ads M[ads] = LS[ls]
ldr r R[r] = LS r = 0..31
str r LS = R[r]
ldx ls r1 r2 LS[ls] = M[R[r1]+R[r2]] load index
stx ls r1 r2 M[R[r1]+R[r2]] = LS[ls] store index
ldw @ads LS = M[ads] load wide
bc r ls R[r] = LS[ls] broadcast

## Slide 9: ALU operations
add r3 r1 r2 R[r3] = R[r1] + R[r2]
sub r3 r1 r2 R[r3] = R[r1] - R[r2]
mul r3 r1 r2 R[r3] = R[r1] * R[r2]
ashr r3 r1 #n R[r3] = R[r1] >> n
addi r3 r1 #n R[r3] = R[r1] + n
and r3 r1 r2 R[r3] = R[r1] & R[r2]
or r3 r1 r2 R[r3] = R[r1] | R[r2]
xor r3 r1 r2 R[r3] = R[r1] ^ R[r2]
lt r3 r1 r2 R[r3] = R[r1] < R[r2]
le r3 r1 r2 R[r3] = R[r1] <= R[r2]
eq r3 r1 r2 R[r3] = R[r1] == R[r2]

## Slide 10: Control
jmp @ads pc = ads
jz r @ads if R[r] == 0, pc = ads
jnz r @ads if R[r] != 0, pc = ads
sys 4 stop simulation
equivalent
inc r addi r r #1
dec r addi r r #-1
clr r xor r r r
mov r3 r1 addi r3 r1 #0

## Slide 11: Multiply two vectors A = B * C
ld 0 @104
ld 1 @105
ld 2 @106
ld 3 @107 ; load B from Mem to LDS
ldr 0 ; move LDS to R[0]
ld 0 @108
ld 1 @109
ld 2 @110
ld 3 @111 ; load C from Mem to LDS
ldr 1 ; move LS to R[1]
mul 2 0 1 ; R[2] = R[0] * R[1] all cores
str 2 ; move R[2] to LS
st 0 @100
st 1 @101
st 2 @102
st 3 @103 ; store LS to Mem
sys 4 ; stop simulation
.end
Let
A at @100..103,
B at @104..107,
C at @108..111,
use
R[2] for A,
R[0] for B,
R[1] for C.

## Slide 12: data
@100
0 0 0 0 ; A
1 2 3 4 ; B
2 3 4 5 ; C
.end

## Slide 13: Loop with jmp, jz, jnz
Because NPU is SIMD (single instruction, multiple data) the condition zero/not-zero must be true for all PEs
they work in lock-step
clr 2
addi 2 2 #n
:loop
; perform some action
dec 2
jnz 2 @loop

## Slide 14: Accessing an array
use LS to indirectly address memory.
access to memory must be "serialised“
ldx ls r1 r2 LS[ls] = M[ R[r1]+R[r2] ]
stx ls r1 r2 M[ R[r1] + R[r2] ] = LS[ls]

## Slide 15: Sum all elements in an array
array is terminated with 0.
i = 0
s = 0
while ax[i] != 0
s = s + ax[i]
i++

## Slide 16: uses all PEs to do the same task
clr 2 ; i = 0
clr 1 ; s = 0
clr 5
addi 5 5 #100 ; base &ax
:loop
ldx 0 5 2 ; get ax[i] to all cores
ldx 1 5 2
ldx 2 5 2
ldx 3 5 2
ldr 3 ; to r3
jz 3 @exit ; ax[i] == 0 ?
add 1 1 3 ; s += ax[i]
inc 2 ; i++
jmp @loop
:exit
sys 4
.end
r1 s, r2 i, r3 ax[i], r5 &ax

## Slide 17: Striping
array 0 1 2 3 4 5 6 7 8 . . .
P0 P1 P2 P3
P0 P1 P2 P3
Px repeat: sx += ax[.]
PE0 PE1 PE2 PE3
partial sum s0 s1 s2 s3
reduction
s += s0
s += s1
s += s2
s += s3

## Slide 18: each PE sums different data
:main ; initialize base and index, r1 base, r2 index ldw @100 ; @100 stores base address ldr 1 ; r1 -- base address ld 0 @101 ; @101 stores 0 initial index ld 1 @102 ; @102 stores 1 ld 2 @103 ; @103 stores 2 ld 3 @104 ; @104 stores 3 ldr 2 ; r2 -- index

## Slide 19
clr 4 ; r4 -- sum = 0
addi 8 4 #2 ; r8 -- loop count #2
; fetch n elements
:loop
ldx 0 1 2 ; ax[i]
ldx 1 1 2
ldx 2 1 2
ldx 3 1 2
ldr 3 ; r3 = ax[i]
add 4 4 3 ; sum += ax[i]
addi 2 2 #4 ; index += 4
dec 8 ; loop count --
jnz 8 @loop

## Slide 20
clr 6 ; r6 sum = 0
str 4
bc 5 0 ; r5s = r4_pe0
add 6 6 5
bc 5 1 ; r5s = r4_pe1
add 6 6 5
bc 5 2 ; r5s = r4_pe2
add 6 6 5
bc 5 3 ; r5s = r4_pe3
add 6 6 5
str 6
st 0 @105 ; @105 result
sys 4
.end
now partial sum is in r4
how to sum all r4s
accumulate it in r6
broadcast each r4 to r5 and r6 += r5

## Slide 21: data
@100
106 0 1 2 3 0 ; base address, 0,1,2,3, result
11 22 33 44 ; @106 ax[.]
55 66 77 88
.end