## Slide 1: Instruction set
Prabhas Chongstitvatana
Chulalongkorn university

## Slide 2: S2 version 1: 32-bit Processor
a typical simple 32-bit CPU
three-address instruction
32 registers and load/store instructions

## Slide 3: S2 processor

## Slide 4: A general format of an instruction
(register to register operations)
op r1 r2 r3 means R[r1] = R[r2] op R[r3]
add r0 r2 r4 R[0] = R[2] + R[4]

## Slide 5: Instruction type
arithmetic: add sub mul div mod
logic: and or xor eq ne lt le gt ge shl shr
control: jmp jt jf jal ret
data: ld st push pop mov

## Slide 6: Arithmetic
two-complement integer arithmetic
n is 17-bit sign extended
add r1 r2 r3 R[r1] = R[r2] + R[r3]
add r1 r2 #n R[r1] = R[r2] + n
sub r1 r2 ... R[r1] = R[r2] - R[r3]
mul r1 r2 ... R[r1] = R[r2] * R[r3]
div r1 r2 ... R[r1] = R[r2] / R[r3] integer div
mod r1 r2 ... R[r1] = R[r2] % R[r3] modulo

## Slide 7: Logic (bitwise)
n is 17-bit sign extended
and r1 r2 r3 R[r1] = R[r2] bit-and R[r3]
and r1 r2 #n R[r1] = R[r2] bit-and n
or r1 r2 r3 R[r1] = R[r2] bit-or R[r3]
or r1 r2 #n R[r1] = R[r2] bit-or n
xor r1 r2 r3 R[r1] = R[r2] bit-xor R[r3]
xor r1 r2 #n R[r1] = R[r2] bit-xor n
eq r1 r2 r3 R[r1] = R[r2] == R[r3]
eq r1 r2 #n R[r1] = R[r2] == n

## Slide 8: Data
d is 17-bit sign extended
m is 22-bit sign extended
ld r1 ads is R[r1] = M[ads] absolute
ld r1 +r2 r3 is R[r1] = M[R[r2]+R[r3]] index
ld r1 @d r2 is R[r1] = M[d + R[r2]] displacement
st r1 ads is M[ads] = R[r1] absolute
st r1 +r2 r3 is M[R[r2]+R[r3]] = R[r1] index
st r1 @d r2 is M[d + R[r2]] = R[r1] displacement
mov r1 #m is R[r1] = m move constant
mov r1 r2 is R[r1] = R[r2] move value

## Slide 9: Control
jmp ads pc = ads jump
jt r1 ads if R[r1]!=0 pc = ads jump if true
jf r1 ads if R[r1]==0 pc = ads jump if false
jal r1 ads R[r1] = PC; PC = ads jump and link
ret r1 PC = R[r1] return

## Slide 10: Special
Stack operation
push r1 r2 is R[r1]++; M[R[r1]] = R[r2]
push r2, r1 as stack pointer
pop r1 r2 is R[r2] = M[R[r1]]; R[r1]--
pop to r2, r1 as stack pointer
Pseudo
  trap r1 #0 stop simulation
  trap r1 #1 print integer in R[r1]
  trap r2 #2 print character in R[r2]

## Slide 11: Instruction format
L-format op:5 rd1:5 ads:22
D-format op:5 rd1:5 rs2:5 disp:17
X-format op:5 rd1:5 rs2:5 rs3:5 xop:12
(rd dest, rs source, ads 22-bit, disp 17-bit sign extended)
fixed length at 32 bits
32 registers.
address space is 32-bit.
access to memory is always on word boundary (no byte-access)
direct (absolute address) is 22-bit or the first 4M words.
index and indirect access can reach the whole 32-bit address space.
immediate value (d) is 17-bit. It is sign extended. jump instructions (jmp, jt, jf) have 22-bit address.

## Slide 12: How to use instructions
a = b + c
let a,b,c be local variables
use r1, r2, r3 to store a,b,c
add r1 r2 r3 R[0] = R[1] + R[2]

## Slide 13: Global variable
a = b + c
let a,b,c be global variables at 100,101,102
use r1, r2, r3 to store values temporary
ld r2 101
ld r3 102
add r1 r2 r3
st r1 100

## Slide 14: simple loop
add 1..10
simple no-loop
use r1 as accumulator for sum
mov r1 #0
add r1 r1 #1
add r1 r1 #2
...
add r1 r1 #10

## Slide 15: use normal loop
pseudo code
s = 0
i = 1
while i <= 10
  s = s + i
  i = i + 1
use r1 as s, r2 as i, r3 as flag
mov r1 #0
mov r2 #1
:loop
le r3 r2 #10
jf r3 exit
add r1 r1 r2
add r2 r2 #1
jmp loop
:exit

## Slide 16: access to an array
add all elements in an array of 10 numbers
pseudo code
ax[10]
  s = 0
  i = 0
  while i < 10
    s = s + ax[i]
    i = i + 1

## Slide 17
to access ax[i]. let ax is at 1000
use r1 as s, r2 as i, r3 as flag, r4 as base, r5 as ax[.]
mov r1 #0
mov r2 #0
mov r4 #1000
:loop
lt r3 r2 #10
jf r3 exit
ld r5 +r4 r2 ; get ax[i]
add r1 r1 r5
add r2 r2 #1
jmp loop
:exit

## Slide 18
Next: assembly language programming