## Slide 1: Pipeline
Prabhas Chongstitvatana
20 Feb 2023

## Slide 2: Instruction cycle
1. instruction fetch
2. instruction decode/register fetch
3. execution/effective address/ALU op
4. memory access
write-back

## Slide 3: Total time for each instruction

## Slide 4: Non-pipe vs pipelined

## Slide 5: Performance in pipeline
Time per instruction in a pipelined processor,
Assume ideal condition (no stall)
Time per instruction on non-pipeline / no. of stages of pipeline
Pipeline improves performance by increases instruction throughput

## Slide 6: Pipeline harzards
Structural harzard
  Not enough hardware unit
Data harzard
  One stage waits on data from another stage
Control harzard
  Stall on branch

## Slide 7: RISC pipeline

## Slide 8: Structural hazard

## Slide 9: Data harzard
add x1, x2, x3
sub x4, x1, x5
Data forwarding

## Slide 10: But still stall in some cases

## Slide 11: Reorder code to avoid stalls
a = b + e;
c = b + f;

## Slide 12: Control harzard

## Slide 13: branch-prediction-buffer
memory stores prediction bit (taken/not taken)
index by lower portion of the address of branch instruction

## Slide 14: one-bit predictor
one-bit predictor
if a branch is always taken, predict incorrectly twice

## Slide 15: One-bit-predictor
1 0000 mov
2 0001 add
3 0010 jmp taken
4 0000 mov
5 0001 add
6 0010 jmp not-taken
7 0011 ld
8 0100 st
9 0101 jmp taken
10 0000 mov
11 0001 add
12 0010 jmp taken
branch prediction buffer
0010 [1] @3 hit,
[1] @6 miss flip,
[0] @12 miss flip -> [1]
0101 [1] @9 hit

## Slide 16: Two-bit-predictor

## Slide 17: Quiz 1
Calculate average execution time (CPI)
a processor has 1 ns clock cycle non-pipeline. it uses 5 cycles for ALU ops, 4 cycles for branch,6 cycles MEM.
frequency of ops: ALU 50%, BR 20%, MEM 30%
What is it average instruction execution time?
average instruction execution time = clock cycle x average CPI
Answer
Assume 1 ns clock
1 ns x [(50%x5) + (20%x4) + (30%x6)]
2.5 + .8 + 1.8 = 5.1

## Slide 18: Quiz 2
This is a trace of instruction execution. using one-bit branch prediction, how many miss?
branch prediction buffer
0011 [1] @4 hit
[1] @8 miss flip
[0] @15 miss flip
[1] @19 miss flip -> [1]
0110 [1] @11 hit
Answer 3 misses
1 0000 add
2 0001 add
3 0010 ld
4 0011 jmp taken
5 0000 add
6 0001 add
7 0010 ld
8 0011 jmp not-taken
9 0100 sub
10 0101 st
11 0110 jmp taken
12 0000 add
13 0001 add
14 0010 ld
15 0011 jmp taken
16 0000 add
17 0001 add
18 0010 ld
19 0011 jmp not-taken
20 0100 sub

## Slide 19: Quiz 3
1 0000 add
2 0001 add
3 0010 ld
4 0011 jmp taken
5 0000 add
6 0001 add
7 0010 ld
8 0011 jmp not-taken
9 0100 sub
10 0101 st
11 0110 jmp taken
12 0000 add
13 0001 add
14 0010 ld
15 0011 jmp taken
16 0000 add
17 0001 add
18 0010 ld
19 0011 jmp not-taken
20 0100 sub
This is a trace of instruction execution. using two-bit branch prediction, how many miss?
Branch prediction buffer
0011 [11] @4 hit
[11] @8 miss -> [10]
[10] @15 hit -> [11]
[11] @19 miss -> [10]
0110 [11] @11 hit
Answer 2 misses

## Slide 20: History of Intel family pipeline

## Slide 21: Example of pipeline in real processor
core i7 branch predictor
uses a two-level predictor that has a smaller first-level predictor, and a larger second-level predictor as a backup.
Each predictor combines three different predictors:
  (1) the simple two-bit predictor,
  (2) a global history predictor,
  (3) a loop exit predictor.

## Slide 22: Misprediction rate of intel i7 6700